## Slide 1
GREEN BUILDING
GROUP 12
VineWeave
Canopy
A tree-like support system for climbing plants
and pedestrian shade
Parametric design · Planting · Shade performance
TEAM & RESPONSIBILITIES
臧唯羽
Form & parametric
modelling
林新淇
Materials &
construction
虞寒哲
Shade performance
& application
徐世程
PPT production
& integration
陈淼
English presentation
& Q&A
Notes: TAKEAWAY VineWeave Canopy is the title and central subject; team credits are secondary. SPOKEN SCRIPT We present VineWeave Canopy, a tree-like support system combining climbing plants with pedestrian shade. Our work connects parametric geometry, material and construction choices, and shading performance. The team responsibilities are summarised below. We begin with the public-space problem and the design goals. TRANSITION First, the public-space problem. Q&A Where are the detailed responsibilities? The names and core roles remain on the cover; the supplied allocation and planning document retain the full task descriptions.

## Slide 2
GREEN BUILDING
DESIGN INTENT
A shaded pause point in public space
Combine climbing vegetation, a tree-like support and clear pedestrian circulation.
Mechanism references: [1,2]. Project design: P4. Thermal improvement is an objective, not a measured result.
02
01
SOLAR EXPOSURE
Offer local shelter for short pedestrian stops.
02
CLIMBING SUPPORT
Guide vegetation across a broad, elevated crown.
03
OPEN CIRCULATION
Keep the surrounding walking route accessible.
Design goal: reduce direct solar exposure while supporting everyday use.
Notes: TAKEAWAY The project targets local shade, not a street-wide cooling claim. SPOKEN SCRIPT Our starting point is a short pedestrian pause in an exposed public space. We combine a broad climbing-plant support with open circulation around it. Shading is intended to reduce direct solar exposure. Actual air-temperature and thermal-comfort changes would still need valid environmental measurements or modelling. TRANSITION Here is the proposed geometry. Q&A How much cooling is achieved? No temperature reduction has been measured or calculated in this project.

## Slide 3
GREEN BUILDING
DESIGN & GEOMETRY
A broad crown on a compact tree-like support
Project geometry—not a certified structural or fabrication model.
Source: project model and geometry records (P1). Dimensions rounded; exterior geometry diameter 80 mm.
03
PLAN
ELEVATION
6.22 × 6.66 m
Overall plan extent
59 MEMBERS
3.48 m MAX. HEIGHT
80 mm EXTERIOR DIAMETER
Notes: TAKEAWAY The geometry creates an elevated climbing envelope while concentrating the supports. SPOKEN SCRIPT The model has fifty-nine members. Its extent is about six point two two by six point six six metres, with a height around three point four eight metres. The plan and elevation show the broad crown and converging supports. These are geometric dimensions, separate from structural verification. TRANSITION Now, the crown layout. Q&A Does a valid model establish safety? No. Closed CAD geometry does not verify member capacity, joints, foundations or wind resistance.

## Slide 4
GREEN BUILDING
DESIGN & GEOMETRY
A climbing envelope with open edges
Organise the crown, central opening and pedestrian edge as one system.
Sources: project geometry and proposed layout (P1, P4). The leaf envelope is hypothetical.
04
01
INTERWOVEN CROWN
Provides the proposed climbing envelope.
02
CENTRAL OPENING
Leaf-hole size is an explicit analysis assumption.
03
OPEN SIDES
Retain space for movement and potential airflow.
Notes: TAKEAWAY The crown, opening and open sides each have a defined design role. SPOKEN SCRIPT The crown provides a framework for climbing plants. The central opening is retained in the analysis, but its future leaf boundary depends on growth and pruning. Around the support, open sides leave space for movement. They express an airflow intention rather than a proven ventilation effect. TRANSITION Next, material roles. Q&A Will the central leaf hole remain open? Only under the stated maintenance assumption; real vegetation could grow across it.

## Slide 5
GREEN BUILDING
MATERIALS
Assign materials by structural role
A proposed steel support zone and engineered-bamboo crown.
Sources: project centreline classification and material schedule (P1, P3). Proposed material assignment—not a safety certification.
05
12 STEEL SUPPORTS
69.38 m · proposed galvanised Q355B tube
47 BAMBOO CROWN MEMBERS
219.28 m · proposed engineered bamboo
Notes: TAKEAWAY Different member roles motivate different materials. SPOKEN SCRIPT Classifying the centre lines by whether they reach the ground gives twelve supports and forty-seven crown members. Steel is proposed for the support zone and engineered bamboo for the crown. The coloured view shows this assignment; neither zone has passed a complete structural analysis. TRANSITION Here are the screening inputs. Q&A Why must the supports be steel? Steel is the proposed choice; a unique-material necessity has not been established by complete load and stability analysis.

## Slide 6
GREEN BUILDING
MATERIALS
Material selection balances several requirements
Preliminary screening inputs; match all bamboo properties to a confirmed product.
Source: material-input workbook (P3). *Reference inputs—not independently verified product data or quotations.
06
MATERIAL | λ* W/(m·K) | CARBON FACTOR* kgCO₂e/kg | DESIGN IMPLICATION
Galvanised steel | 50 | 2.15 | Proposed supports; protect against corrosion.
Engineered bamboo* | 0.22 | 0.40 | Proposed crown; stiffness and treatment need confirmation.
Treated timber | 0.14 | 1.10 | Screened alternative; capacity and outdoor care matter.
Product identity, strength, stiffness and carbon boundaries still require evidence.
Notes: TAKEAWAY Screening values help frame a choice but do not replace product-specific evidence. SPOKEN SCRIPT This is a preliminary screen, not a certified specification. The conductivity and carbon factors are workbook inputs. The bamboo product identity, strength, stiffness, density and carbon data must be matched consistently before final selection. A favourable material factor alone does not establish a feasible system. TRANSITION Connection restraint is the next condition. Q&A Are glubam and scrimber interchangeable? No. Their manufacturing routes and properties can differ, so we retain the generic engineered-bamboo label for now.

## Slide 7
GREEN BUILDING
STRUCTURAL FEASIBILITY
Connection restraint governs deflection
A simplified beam check—not a verified response of the complete canopy.
Source: simplified deflection workbook (P3). Bamboo inputs and actual joint restraint require verification.
07
Chart: 
| Simply supported | Ideal fixed ends
Deflection / adopted limit | 3.02 | 0.6
SAME 6.65 m SPAN
Self-weight + assumed wet foliage
RATIO ≤ 1.0 IS THE TARGET
Actual rotational restraint is not verified.
Deflection / adopted L/200 limit
Notes: TAKEAWAY The calculation identifies a restraint requirement, not a proven joint solution. SPOKEN SCRIPT Here the same six point six five metre member is checked under two ideal boundary conditions. Relative to the adopted deflection limit, the simply supported result is about three, while the ideal fixed-end result is about zero point six. This illustrates why connection restraint matters. It does not prove that twelve proposed nodes provide these restraints throughout the complete canopy. TRANSITION This also affects the budget. Q&A Have the joints passed? No. A detailed joint and global structural model, with verified material inputs, is still required.

## Slide 8
GREEN BUILDING
COST & CARBON
A preliminary budget of CNY 51,676 per unit
The total includes more than the visible structural members.
Source: Cost-Analysis.xlsx (P3). Preliminary estimate—not supplier quotations; node price is particularly uncertain.
08
Chart: 
| Materials | Installation | Other | Fabrication | Maintenance | Planting | Transport
Cost / CNY | 30549.3023 | 6050 | 5679.6829 | 5241.7335 | 2300 | 1165 | 690
CNY 51,676
Preliminary total per unit
CNY 12,000
Rigid-node allowance within materials
Notes: TAKEAWAY Connections form a substantial part of the estimated cost. SPOKEN SCRIPT The estimated unit total is about fifty-one thousand six hundred and seventy-six yuan. The chart includes materials, fabrication, transport, installation, planting, maintenance and other costs. Nodes account for twelve thousand yuan within materials. These are preliminary allowances, not supplier quotations. TRANSITION Next, the carbon contributors. Q&A Is the price confirmed? No. Node fabrication and the other rates require actual supplier and contractor quotations.

## Slide 9
GREEN BUILDING
COST & CARBON
Track embodied carbon—and long-term care
Current factors indicate where further checking and reduction efforts should focus.
Source: workbook carbon estimate (P3). Preliminary factors; boundaries, processing and node inclusion need verification.
09
Chart: 
| Primary members | Counterweight | Other components
Carbon / kgCO₂e | 1581.1963 | 1088.64 | 150
≈ 2,820
kgCO₂e / unit
Primary members
1,581
Counterweight
1,089
Other components
150
Protect steel • Treat bamboo • Inspect joints
Notes: TAKEAWAY The estimate is useful for identifying contributors, but its boundary is not yet certified. SPOKEN SCRIPT The preliminary total is about two thousand eight hundred and twenty kilograms of carbon-dioxide equivalent per unit. Primary members contribute the largest share, while the counterweight contributes roughly thirty-nine percent. The bamboo factor, processing boundary and allowance for connection components still need verification. We do not credit biogenic carbon storage or present this as a verified whole-life assessment. TRANSITION Now, the planting requirements. Q&A Is this verified A1–A3 carbon? Not yet. Factor-specific boundaries must first be aligned and checked.

## Slide 10
GREEN BUILDING
PLANTING
Plant choice is part of the performance design
Proposed candidates—not a confirmed site-specific planting specification.
Source: project planting screen (P3). Local suitability, wet loads and phenology require confirmation.
10
Boston ivy
Primary candidate
Tendrils with adhesive pads
Check anchorage and seasonal cover.
Trumpet creeper
Alternative
Aerial roots
Manage vigorous growth and root space.
Rangoon creeper
Companion candidate
Twining shoots
Confirm local winter survival and leaf habit.
Root space • Water supply • Training • Pruning
Notes: TAKEAWAY Choose plants through their climbing behaviour, local suitability and maintenance needs. SPOKEN SCRIPT These are candidate plants from the project screen. Boston ivy, trumpet creeper and Rangoon creeper climb in different ways. Their suitability must be checked against local climate, anchorage, root space and maintenance. In particular, we have not established a common seasonal pattern or a reliable time to full canopy cover. TRANSITION Next, the environmental intention. Q&A How soon will the plants cover the canopy? No growth duration has been calibrated; species, site and care evidence are needed.

## Slide 11
GREEN BUILDING
ENVIRONMENTAL INTENT
Open sides and a porous crown
Shade and potential airflow paths are design intentions with different evidence needs.
Mechanisms: [1,2]. Airflow sketch: project concept (P4), not a wind-field simulation.
11
CONCEPTUAL AIRFLOW
01
SHADE
Reduce direct solar exposure. [1,2]
02
OPEN EDGES
Retain potential lateral airflow paths.
03
FOLIAGE DENSITY
More cover may also increase flow resistance.
Notes: TAKEAWAY Shading and airflow should not be treated as the same type of result. SPOKEN SCRIPT Shading is the direct geometric mechanism studied here. The open edges retain potential lateral airflow paths, but dense vegetation may also resist airflow. The dashed arrows describe an intention, not simulated wind. We do not infer a chimney effect from the central opening or transfer a cooling number from a different greening project. TRANSITION Here are the analytical assumptions. Q&A Does the opening improve ventilation? It is a hypothesis. A site-specific flow model or measurement is needed to establish an effect.

## Slide 12
GREEN BUILDING
ANALYSIS METHOD
Make the assumptions—and the metrics—explicit
One fixed reference zone; two different shade metrics.
Solar method: NOAA [3]. Reference zone and optical scenarios: project analysis (P2, P5).
12
30°N
Illustrative location
09:00–15:00
True solar time
23.23 m²
5 × 5 m minus r = 0.75 m
ASSUMED FOLIAGE
No site obstructions
IDEAL GEOMETRIC OVERLAP
Continuous-leaf shadow intersecting the reference zone.
EQUIVALENT DIRECT-BEAM BLOCKAGE
Frame + leaf patches; overlap deducted; τ = 0.15.
Notes: TAKEAWAY The following percentages are meaningful only with their metric and assumptions. SPOKEN SCRIPT We assume thirty degrees north, true solar time and no surrounding obstructions. The target is a fixed reference zone, not net usable floor area. Ideal overlap uses a continuous leaf envelope. Equivalent blockage adds the frame, spatial leaf patches and assumed transmittance. Neither metric is a temperature change. TRANSITION First, the ideal shadow footprint. Q&A Why two metrics? One isolates geometric overlap; the other adds explicit frame and optical assumptions. Their percentages should not be substituted for each other.

## Slide 13
GREEN BUILDING
SHADE RESULTS
Noon overlap does not mean all-day shade
Ideal continuous-leaf overlap within the fixed reference zone.
Source: project geometric projection (P2). Summer solstice; 30°N; assumed leaf envelope and orientation.
13
09:00 SOLAR TIME
47.2%
12:00 SOLAR TIME
98.7%
15:00 SOLAR TIME
47.2%
09:00–15:00 TIME MEAN: 75.3%
Notes: TAKEAWAY The position of the shadow matters as much as the noon percentage. SPOKEN SCRIPT The three views use the same scale and target. At nine and fifteen solar time, ideal overlap is about forty-seven percent. At noon it reaches nearly ninety-nine percent, while the six-hour mean is seventy-five point three percent. This is a hypothetical continuous-leaf envelope. It is not a prediction that real vegetation will provide continuous shade throughout the day. TRANSITION Next, crown width at fixed cover. Q&A Does 98.7 percent describe actual planting? No. It is the ideal leaf-envelope geometric overlap at solstice noon under the stated assumptions.

## Slide 14
GREEN BUILDING
PARAMETER STUDY
Crown width changes useful shade
Same target and 50% plan cover; wider crowns also require more material and planted area.
Source: parameter and spatial-cover simulation (P5). Solstice 09–15 mean; τ = 0.15; assumed conditions.
14
Chart: 
| Smaller crown | Baseline | Larger crown
Mean direct-beam blockage (%) | 52.2795 | 60.1972 | 66.1435
MEAN EQUIVALENT DIRECT-BEAM BLOCKAGE
Notes: TAKEAWAY A larger crown increases blockage in this controlled comparison, not necessarily overall design quality. SPOKEN SCRIPT At fifty percent plan cover, increasing crown width raises mean equivalent blockage from fifty-two point three to sixty point two and sixty-six point one percent. But the larger crown requires more member length and more planted area. The comparison does not hold inputs equal or establish an optimum. TRANSITION Now, cover at fixed geometry. Q&A Is the larger model the best design? Shade is only one criterion; structural capacity, space, material and maintenance have not been jointly optimised.

## Slide 15
GREEN BUILDING
PLANT-COVER SCENARIOS
Foliage development changes blockage
Fixed structure; cover scenarios have no assigned growth months or years.
Source: spatial-cover simulation (P5). Solstice 09–15 mean; frame/leaf overlap deducted; τ = 0.15.
15
VIEW SEQUENCE: 0 → 20 → 50 → 80 → 95% PLAN COVER
Chart: 
| 0% plan cover | 50% plan cover | 95% plan cover
Mean equivalent direct-beam blockage (%) | 40.2187 | 60.1972 | 70.6955
MEAN DIRECT-BEAM BLOCKAGE
Notes: TAKEAWAY Coverage is a spatial scenario, not a biological timetable. SPOKEN SCRIPT The frame already blocks some sunlight before foliage develops. Holding the structure fixed, the zero, fifty and ninety-five percent cover scenarios give mean direct-beam blockage of about forty, sixty and seventy-one percent. The animation includes two additional intermediate states. These are nested spatial-cover scenarios, not a timetable for real plant growth or a measured seasonal cycle. TRANSITION Next, relate shade to occupied space. Q&A How many years to ninety-five percent? We have not calibrated growth duration. That requires species, site, planting and maintenance evidence.

## Slide 16
GREEN BUILDING
APPLICATION
Place seating for the occupied hours
Illustrative shade movement—not a real site or a compliance drawing.
Sources: project design and fixed-50%-cover projection (P4, P5). Proposed comfort validation may follow [4].
16
FIXED 50% PLAN COVER • SOLAR TIME 09:00 → 15:00
01
FOLLOW THE SHADE
Use occupied-hour footprints, not only noon.
02
KEEP ROUTES CLEAR
Separate stopping places from through movement.
03
ALLOW FOR PLANT CARE
Reserve roots, water and maintenance access.
Notes: TAKEAWAY A useful shade calculation must eventually use the real occupied area. SPOKEN SCRIPT The cover stays at fifty percent as the sun changes direction. Seating should follow occupied-hour shade, rather than only the support centre or noon footprint. A real layout must also account for the counterweight, roots and circulation. This reference square is not a verified net usable area. TRANSITION Finally, the assembly strategy. Q&A Is this a real street layout? No. A site-specific plan and paired environmental validation are still needed.

## Slide 17
GREEN BUILDING
CONSTRUCTION
Prefabricate components; manage site complexity
Proposed assembly logic—not a tested construction programme.
Sources: project build-up and cost workbook (P3, P4). Labour, curing, transport and lifting assumptions require confirmation.
17
01
PREFABRICATE
Form, treat and number
02
POSITION BASE
Lift and align
03
ASSEMBLE
Support and crown
04
GROUT & CURE
Verify node details
05
INSPECT & PLANT
Check, train and irrigate
14 PERSON-DAYS
Current labour estimate—not 14 calendar days
GROUTED NODES NEED CURING
Full dry assembly and lossless reversal are not established.
Notes: TAKEAWAY Prefabrication is an opportunity; the node detail is a construction constraint. SPOKEN SCRIPT The proposal uses factory forming, treatment, preassembly and numbering before site installation. The simplified sequence then positions the base, assembles the frame, grouts and cures the nodes, and finishes with inspection and planting. The workbook estimates fourteen person-days, not fourteen calendar days. Grouting also means that completely dry, losslessly reversible construction should not be claimed. TRANSITION We close with the main contribution. Q&A Can it be easily moved? Relocation and individual replacement depend on the final joints, lifting design and foundation arrangement; they are not yet verified.

## Slide 18
GREEN BUILDING
CONCLUSION
Useful shade—with a clear path to validation
VineWeave Canopy integrates form, planting and a proposed build-up.
Project synthesis (P1–P5). Scenario evidence supports the concept, not an engineering or measured-comfort certification.
18
01
AN INTEGRATED SUPPORT
Tree-like geometry and climbing vegetation for local shade.
02
EXPLICIT PERFORMANCE SCENARIOS
Geometry, cover and sun position jointly shape useful blockage.
03
A DEFINED NEXT STEP
Confirm products, joints and site conditions; then validate outcomes.
Notes: TAKEAWAY The contribution is a traceable concept and scenario analysis, with implementation conditions stated clearly. SPOKEN SCRIPT VineWeave combines a tree-like support, climbing vegetation and a proposed material and assembly strategy. The analysis shows how geometry, foliage and sun position affect shade within an explicit target. The next stage is to confirm the bamboo product, connection behaviour and real site conditions before claiming structural or thermal performance. Thank you; we welcome your questions. TRANSITION Thank you. We welcome your questions. Q&A What is the strongest demonstrated result? The traceable geometric and direct-beam shade scenarios, under their stated assumptions.

## Slide 19
GREEN BUILDING
REFERENCE / Q&A
Sources and evidence boundaries
Published-source leads and supplied project records are distinguished.
Literature details were supplied with the project; original-source verification remains pending.
19
[1] OUTDOOR SHADE & COMFORT
Watanabe et al. (2014). Evaluation of outdoor thermal comfort in sunlight, building shade, and pergola shade during summer in a humid subtropical region. Building and Environment, 82, 556–565.
[2] GREENING MECHANISMS
Hoelscher et al. (2016). Quantifying cooling effects of facade greening: Shading, transpiration and insulation. Energy and Buildings, 114, 283–290.
[3] SOLAR GEOMETRY
NOAA Global Monitoring Division. General Solar Position Calculations.
gml.noaa.gov/grad/solcalc/solareqns.PDF
[4] COMFORT METHOD
UTCI Calculator / COST Action 730.
www.utci.org/utci_calc.php
Method reference only; no project UTCI result is claimed.
PROJECT RECORDS
P1 Model & take-off • P2 Ideal shade analysis • P3 Cost-Analysis.xlsx
P4 Proposed design & build-up • P5 Parameter and spatial-cover simulation
Unverified product factors, growth duration, actual joint restraint and field thermal response remain open.
Notes: TAKEAWAY References support methods and mechanisms; project evidence remains distinct. SPOKEN SCRIPT This slide is available for questions and is not part of the planned spoken sequence. Literature and method entries are source leads supplied in the project material; their original-source checks remain pending. Project records identify the model, calculations, estimate and proposals. TRANSITION Return to the relevant result slide during questions. Q&A Do the references validate all material factors? No. Product properties, specific standards and factor boundaries require further checks.