## Slide 1
GREEN BUILDING
GROUP 12
VineWeave
Canopy
A tree-like climbing-plant support
for pedestrian shade
Parametric design · Planting · Shade performance
TEAM & RESPONSIBILITIES
臧唯羽
Form & parametric
modelling
林新淇
Materials &
construction
虞寒哲
Shade performance
& application
徐世程
PPT production
& integration
陈淼
English presentation
& Q&A
Notes: TAKEAWAY Introduce the project before the team credits. SPOKEN SCRIPT VineWeave Canopy combines climbing plants with a tree-like support to provide pedestrian shade. Our group connects parametric geometry, material and construction choices, and shading analysis. The names below identify our responsibilities. We will explain both the design decisions and the evidence supporting them. TRANSITION First, the design brief. Q&A Where are the full roles? The cover retains the core allocation; the planning document records the complete supplied descriptions.

## Slide 2
GREEN BUILDING
BRIEF & STRATEGY
Translate the brief into five design decisions
A public shade facility must connect environmental intent with a buildable support.
Shade/greening mechanisms: [1,2]. Project requirements and proposed strategy: P4.
02
COURSE REQUIREMENT | OUR RESPONSE | WORK PRODUCED
Structure and materials | Steel supports + proposed bamboo crown | Material screen, member schedule and node concept
Geometric parameters | Control crown width, height and corners | Rhino/GH geometry, plans and parameter models
Shade and airflow | Broad crown + planting + open sides | Shadow projection; conceptual airflow analysis
Plant integration | Screen climbers and organise maintenance | Candidate screen, 2+1 planting proposal, cover scenarios
Assembly and use | Prefabricate, assemble and check occupied-hour shade | Build-up sequence, budget and rest-node application
The design is assessed as a system—not as an isolated shape.
Notes: TAKEAWAY Each course requirement is linked to a visible design response and a work product. SPOKEN SCRIPT The brief asks for more than a tree-like form. We connect materials, geometry, environmental performance, planting and assembly. This table shows the response and the work produced for each requirement. Shade has been calculated under explicit assumptions; airflow and real thermal comfort remain design and validation questions. TRANSITION Next, the geometry and drawing definitions. Q&A Does every row have an experiment? No. We distinguish model outputs, calculated scenarios, preliminary estimates and design proposals.

## Slide 3
GREEN BUILDING
GEOMETRY & DRAWINGS
Define the final geometry—and how it is measured
Dimensioned plan/elevation views; a final parameter schedule, separate from sensitivity settings.
Model records P1 and supplemental geometric check. Centre-line views; exterior dimensions rounded. Drawing sheets accompany the PPT.
03
6.22 m
6.66 m
PLAN
3.48 m
ELEVATION
Curved support inclination is defined by its endpoint chord, not a local tangent.
FINAL PARAMETER | VALUE / DEFINITION
Overall height | ≈3.48 m
Plan extents | ≈6.22 × 6.66 m
Maximum horizontal span | ≈6.91 m, exterior mesh
Support inclination* | 45.9–50.7° to horizontal
Member exterior diameter | 80 mm
Corner / expansion | 0.85 / 1.08
*Angle of each ground-reaching centre-line endpoint chord. Not a uniform member slope.
Notes: TAKEAWAY Final dimensions need explicit definitions and readable technical views. SPOKEN SCRIPT The final geometry has an overall height of about three point four eight metres and a plan extent of six point two two by six point six six metres. Its approximate maximum horizontal exterior span is six point nine one metres. For these curved supports, inclination is defined by the endpoint chord above horizontal. The accompanying drawing sheets explain that definition and the measured range. TRANSITION Next, link those features to environmental potential. Q&A Is 6.91 metres a circular diameter? No. It is the maximum pair distance in the projected exterior mesh, not a foliage diameter or net usable width.

## Slide 4
GREEN BUILDING
FORM & COOLING LOGIC
Connect structural features to cooling potential
A feature–mechanism–benefit chain distinguishes calculated shade from conditional thermal responses.
Project analysis P2/P5 and design P4; general shade/greening mechanisms [1,2]. No measured temperature or airflow improvement is claimed.
04
FEATURE | MECHANISM | EXPECTED BENEFIT | EVIDENCE / CONDITION
Broad crown + climbers | Intercept direct sun above the target | Less solar exposure of people and ground | Geometric and optical shade calculated (P2/P5)
Leaf cover and its position | Change transmission and frame/leaf overlap | Useful shade depends on amount and location | Five cover states + distribution tests (P5)
Open sides and crown porosity | Retain potential paths; foliage may add drag | Possible airflow trade-off, not a proven gain | Qualitative layout intent; no flow simulation
Healthy plants + water | Evapotranspiration depends on plant and water status | Potential latent heat exchange | Mechanism reference [2]; not modelled here
The crown and open edges support the design logic; shading percentages are not cooling degrees.
Notes: TAKEAWAY The required logic links a structural feature to a physical process without overstating the evidence. SPOKEN SCRIPT The table makes the design logic explicit. Crown geometry and foliage intercept direct sun, while cover placement changes transmission and overlap. Open sides retain potential airflow paths, but dense foliage can resist flow. Plant water exchange is another conditional mechanism. We have calculated shade scenarios; we have not measured a temperature reduction or simulated wind. TRANSITION Material assignment follows the structural roles. Q&A Does the opening prove a chimney effect? No. It is a geometric feature and design hypothesis, not a verified airflow result.

## Slide 5
GREEN BUILDING
MATERIAL STRATEGY
Separate the support role from the crown role
Classify members by whether their centre lines reach the ground.
Project take-off and proposed member schedule (P1, P3). Sections and material mass remain preliminary specifications.
05
ZONE | PROPOSED SECTION | LENGTH
12 steel supports | Q355B tube Ø80 × 4 mm | 69.38 m
47 bamboo crown members | Engineered bamboo solid Ø80 mm | 219.28 m
TOTAL | 59 members | 288.66 m
Steel supports address compression and wind bending. The bamboo crown is governed by stiffness, treatment and replaceability.
Notes: TAKEAWAY The quantity schedule links a clear material role to a specific part of the model. SPOKEN SCRIPT The take-off gives twelve ground-reaching supports and forty-seven crown members, with a total centre-line length of two hundred and eighty-eight point six six metres. We propose an eighty-by-four millimetre steel tube for supports and solid engineered bamboo for the crown. This is a material strategy, not proof that either zone is safe. TRANSITION Next, the material-screening criteria. Q&A Does the exterior model contain the final wall thickness? No. The pipe exterior and proposed material section must be distinguished.

## Slide 6
GREEN BUILDING
MATERIAL SELECTION
Five criteria guide the material selection
Durability · cost · thermal conductivity · carbon · environmental adaptability.
Source: material-comparison workbook (P3). *Preliminary inputs; product, processing and factor boundaries need verification.
06
MATERIAL / SECTION | BENDING* kN·m | λ* W/(m·K) | CARBON* kgCO₂e/kg | MATERIAL COST* CNY / 288.66 m
Q355B tube Ø80×4 | 6.14 | 50 | 2.15 | 18,394
Q355B tube Ø80×3 | 4.78 | 50 | 2.15 | 13,983
Engineered bamboo Ø80 | 1.01 | 0.22 | 0.40 | 10,158
Treated timber Ø80 | 0.85 | 0.14 | 1.10 | 6,530
Raw bamboo Ø80 | 0.40 | 0.18 | 0.25 | 4,330
DURABILITY | ENVIRONMENTAL ADAPTABILITY
Protect steel coatings; treat bamboo; detail inspection and replacement. | Check moisture, UV, wind exposure, local supply and plant suitability.
Notes: TAKEAWAY Material screening includes mechanical and practical conditions, not only carbon. SPOKEN SCRIPT These are preliminary screening inputs. Each cost column assumes the same full member length; it is not the adopted unit budget. Steel offers much greater nominal bending capacity. Engineered bamboo is proposed for the crown, but stiffness, treatment and product-specific evidence are essential. Raw bamboo’s low reference cost does not remove its variability and maintenance issues. TRANSITION Crown stiffness leads directly to the connection question. Q&A Are these all verified design values? No. They are workbook screening inputs, and the bamboo identity and properties must be confirmed consistently.

## Slide 7
GREEN BUILDING
CONNECTIONS
The crown is stiffness-sensitive: joints matter
Load assumption → boundary condition → deflection → required connection behaviour.
Simplified beam calculation and proposed node method (P3). Wet foliage 18 kg/m² and bamboo properties are assumed inputs.
07
Chart: 
| Simply supported | Ideal fixed ends
Deflection / mm | 100.5334 | 20.1067
6.65 m SPAN · ADOPTED L/200 = 33.25 mm
PROPOSED SUPPORT-HEAD NODE
Node plate + sleeve + structural adhesive
with high-strength bolts
Concept only; rotational restraint must be verified.
Notes: TAKEAWAY Ideal fixed-end behaviour is a requirement to investigate, not an achieved joint property. SPOKEN SCRIPT The workbook applies self-weight and an assumed wet-foliage load. At the six point six five metre span, the simplified deflection changes from about one hundred millimetres under simple supports to twenty under ideal fixed ends. The adopted limit is thirty-three point two five millimetres. Actual joint and whole-frame stiffness still require verification. TRANSITION Connection complexity also affects the budget. Q&A Do twelve nodes fix every crown member? That has not been demonstrated. Joint rotation and global load transfer still require modelling or testing.

## Slide 8
GREEN BUILDING
BUDGET
The unit budget includes fabrication, installation and care
Preliminary total: CNY 51,676 per unit—not simply the price of the members.
Source: Cost-Analysis.xlsx (P3). All rates remain reference estimates rather than confirmed quotations.
08
Chart: 
| Materials | Installation | Other | Fabrication | Maintenance | Planting | Transport
CNY | 30549.3023 | 6050 | 5679.6829 | 5241.7335 | 2300 | 1165 | 690
MATERIALS = 59.1% OF TOTAL
KEY COMPONENT | CNY
Bamboo crown | 7,716
Steel supports | 4,421
12 rigid-head nodes | 12,000
Counterweight | 3,402
These component rows are part of the full total. Nodes are a larger allowance than the primary steel members.
Notes: TAKEAWAY The budget makes the node trade-off visible. SPOKEN SCRIPT The preliminary total is approximately fifty-one thousand six hundred and seventy-six yuan. Materials are fifty-nine percent of this total; the other categories include fabrication, installation and care. Within materials, twelve proposed nodes account for twelve thousand yuan, more than the primary steel members. The component table is only part of the overall cost, not an additional total. TRANSITION Next, the carbon and maintenance picture. Q&A Are the node prices confirmed? No. They are the most uncertain allowance and need a defined detail and supplier quotation.

## Slide 9
GREEN BUILDING
CARBON & MAINTENANCE
Account for the members, base and maintenance needs
Current carbon estimate: approximately 2,820 kgCO₂e per unit.
Workbook estimate (P3). Factor boundaries and node inclusion require checking; no biogenic-carbon credit is taken.
09
Chart: 
| Primary members | Counterweight | Other components
kgCO₂e | 1581.1963 | 1088.64 | 150
≈ 2,820
kgCO₂e / unit
CONTRIBUTOR | kgCO₂e
Primary members | 1,581
Counterweight | 1,089
Other components | 150
Counterweight ≈ 39% of the current estimate
STEEL | BAMBOO | CONNECTIONS
Protect coating | Treat and inspect | Check fixings and grout
Notes: TAKEAWAY The estimate helps identify contributors and care responsibilities. SPOKEN SCRIPT The primary members and counterweight dominate the current carbon estimate. The counterweight contributes about thirty-nine percent, so foundation decisions also matter. We show the adopted estimate rather than claiming a verified life-cycle result. Outdoor performance also needs coating care, bamboo treatment and connection inspection. Product factors and the allowance for actual node materials still require checking. TRANSITION Plant choice adds another set of requirements. Q&A Is stored biological carbon deducted? No. It is not credited in this estimate, and factor boundaries are not yet fully aligned.

## Slide 10
GREEN BUILDING
PLANTING STRATEGY
Select climbers for support, season and maintenance
The source proposal combines two Boston ivy plants with one Rangoon creeper per unit.
Project planting screen and schedule (P3): eight candidates. Proposed mix; local suitability, attachment and wet loads still need evidence.
10
CANDIDATE / ROLE | CLIMBING METHOD | DESIGN CHECK
Boston ivy — primary | Tendrils with adhesive pads | Attachment and seasonal coverage
Trumpet creeper — alternative | Aerial roots | Vigorous growth and root control
Rangoon creeper — companion | Twining shoots | Local winter survival and leaf habit
2 + 1 PLANTS / UNIT
2 Boston ivy + 1 Rangoon creeper
ROOTS + WATER + TRAINING
Source allowance: 1.2 m³ substrate and a drip system.
Screening also considered wisteria (weight), honeysuckle and firecracker vine (winter leaf retention), and English ivy / star jasmine (leaf retention and public-space checks).
Notes: TAKEAWAY The proposal has a specific planting mix and a screening logic. SPOKEN SCRIPT The source screen considered eight climbers. It proposes Boston ivy as the primary plant, Rangoon creeper as a companion, and trumpet creeper as an alternative. The unit allowance is two ivy plants, one creeper, substrate and drip irrigation. The mix remains subject to local suitability and attachment checks. TRANSITION Plant choice raises the question of when shade becomes available. Q&A Is Rangoon creeper confirmed for the site? No. Climate, winter survival and leaf habit must be checked before adopting the mix.

## Slide 11
GREEN BUILDING
ESTABLISHMENT & USE
Opening the structure is not the same as a mature canopy
Two readiness gates: structural acceptance and an agreed occupied-hour shade target.
Source care/assembly proposals: P3, P4. Coverage stages: P5, not a calibrated biological timeline.
11
ENGINEERING TRACK
Install & grout
Cure & inspect
Accept for opening
VEGETATION TRACK
Plant & train
Expand across crown
Check shade readiness
TIME TO TARGET COVER: NOT YET ESTABLISHED
Month/year estimates need species, local climate, nursery starting size and maintenance evidence. The supplied 0–95% stages do not provide those durations.
Sequence only; intervals are not to scale. Neither 14 person-days nor a 3-year care budget predicts canopy maturity.
Notes: TAKEAWAY The new timeline clarifies what is known and what is still missing. SPOKEN SCRIPT There are two readiness gates. The structure can open only after the required acceptance conditions, while vegetation must reach an agreed shade target during occupied hours. The provided cover scenarios have no growth durations. We therefore show the sequence without invented months or years. Nursery starting size, species, climate and maintenance data are needed to estimate when the target can be met. TRANSITION We next separate the environmental mechanisms. Q&A How long until full use? The current evidence does not support a month estimate. Structural acceptance and vegetation shade readiness must be assessed separately.

## Slide 12
GREEN BUILDING
ANALYSIS METHOD
Project shade onto one fixed reference zone
30°N · assumed X=east/Y=north · true solar time 09–15 · no surrounding obstructions.
Solar geometry: NOAA [3]. Project calculations and scenario assumptions: P2, P5. Foliage/transmittance are not measured.
12
01
SUN DIRECTION
02
MODEL + LEAF ENVELOPE
03
GROUND PROJECTION
04
TARGET INTERSECTION
IDEAL GEOMETRIC OVERLAP
Continuous-leaf shadow ∩ target
÷ target area
EQUIVALENT DIRECT-BEAM BLOCKAGE
Aeq = Abare + (1 − τ)(Aleaf − Aoverlap)
Divide Aeq by target area; τ = 0.15.
TARGET: 5 × 5 m MINUS r = 0.75 m → 23.23 m²
Not net usable floor area.
Notes: TAKEAWAY One calculation isolates leaf-envelope geometry; the other includes frame and optical effects. SPOKEN SCRIPT We project the geometry along the solar direction and intersect it with the same target. The fixed target excludes a central disk. Ideal overlap uses a continuous leaf envelope. Equivalent blockage includes opaque frame shadows and assumed leaf transmittance, with overlap deducted. The two metrics are different, and neither is a temperature change. TRANSITION First, the ideal time-dependent result. Q&A Was numerical resolution checked? The supplied package includes raster spot checks; five versus two-point-five millimetre results differ by up to about 1.06 percentage points in those samples, not as an overall error bound.

## Slide 13
GREEN BUILDING
SHADE PERFORMANCE
The shadow position and solar season both matter
Ideal continuous-leaf overlap: a high noon value does not mean continuous occupied-hour shade.
Project projection data (P2, P5). Solar-season comparison, not a calibrated seasonal plant-growth model.
13
09:00
47.2%
12:00
98.7%
15:00
47.2%
Chart: 
| 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00
Solstice | 47.1557 | 50.9552 | 55.0701 | 60.0396 | 65.5065 | 70.7724 | 75.7958 | 81.0188 | 86.3834 | 91.723 | 95.7667 | 97.9518 | 98.7248 | 97.9518 | 95.7667 | 91.723 | 86.3834 | 81.0188 | 75.7958 | 70.7724 | 65.5065 | 60.0396 | 55.0701 | 50.9552 | 47.1557
Equinox | 21.8064 | 29.6871 | 35.1348 | 38.2326 | 40.8438 | 44.4212 | 49.7525 | 54.7234 | 59.3674 | 63.7194 | 67.5362 | 69.0651 | 69.5586 | 69.0651 | 67.5362 | 63.7194 | 59.3674 | 54.7234 | 49.7525 | 44.4212 | 40.8438 | 38.2326 | 35.1348 | 29.6871 | 21.8064
09–15 TIME MEAN
Solstice 75.3%
Equinox 49.8%
Notes: TAKEAWAY Read the footprint and the whole time window, not only the noon peak. SPOKEN SCRIPT The solstice footprint overlaps about forty-seven percent of the target at nine and fifteen solar time, and almost ninety-nine percent at noon. The curve adds the intervening hours and an equinox solar case. Their means are about seventy-five and fifty percent. This is a comparison of solar conditions under hypothetical foliage, not a seasonal growth forecast. TRANSITION We then change one geometric control at a time. Q&A Does winter use the equinox result? No. Winter solar conditions and plant leaf states would need their own inputs.

## Slide 14
GREEN BUILDING
GEOMETRY SENSITIVITY
Seven models test three geometry controls
One variable at a time; same target, 50% plan cover, solstice solar hours and τ = 0.15.
Project parameter study (P5). Controls are not uniform scaling; larger cover percentage does not imply equal plant/material input.
14
SMALLER CROWN
BASELINE
LARGER CROWN
CONTROL | TESTED SETTINGS | MEAN BLOCKAGE: LOW / BASE / HIGH
Upper expansion | 0.92 / 1.08 / 1.24 | 52.3% / 60.2% / 66.1%
Upper-height control | −0.4 / 0 / +0.4 m | 62.6% / 60.2% / 57.8%
Corner factor | 0.55 / 0.85 / 1.00 | 61.8% / 60.2% / 59.1%
Notes: TAKEAWAY The crown-width result is part of a broader seven-model parameter study. SPOKEN SCRIPT The work includes width, upper-height control and corner factor, with a shared baseline. At fifty percent cover, mean blockage rises from fifty-two point three to sixty-six point one percent as the crown expands. The table records the other controls too. These are controlled shade comparisons, not proof of an optimum or of structural safety after changing geometry. TRANSITION Next, keep the structure fixed and change foliage. Q&A Does the height control shift the whole model by 0.4 metres? No. It is smoothly weighted; actual maximum heights must be read from the geometry records.

## Slide 15
GREEN BUILDING
SPATIAL PLANT COVER
Coverage amount alone does not determine useful shade
Fixed final structure; five nested leaf-cluster scenarios, not observed growing months.
Project spatial-cover calculation (P5). Frame/leaf overlap deducted, τ = 0.15; equivalent direct-beam blockage, not cooling.
15
Chart: 
| 0% | 20% | 50% | 80% | 95%
09–15 mean blockage (%) | 40.2187 | 48.6371 | 60.1972 | 67.9113 | 70.6955
PLAN COVER (%)
VIEW SEQUENCE: 0 → 20 → 50 → 80 → 95% PLAN COVER
Same 50% cover, different layouts at noon: 77.5% / 71.4% / 62.6% blockage.
Notes: TAKEAWAY The package tests both cover quantity and where that cover is placed. SPOKEN SCRIPT The five plan-cover states give mean blockage of about forty, forty-nine, sixty, sixty-eight and seventy-one percent. Bare members already provide shade at zero leaf cover. At the same fifty percent cover, three spatial layouts also produce different noon results. Coverage percentage therefore does not describe where useful shade falls, and the stages do not predict biological growth duration. TRANSITION We connect that moving footprint to public use. Q&A Why is 95% cover not 95% blockage? Target intersection, frame overlap, leaf placement and transmittance all affect the metric.

## Slide 16
GREEN BUILDING
APPLICATION
Put occupied-hour shade into the layout decision
A rest node must coordinate seating, through movement, roots and a substantial base.
Conceptual application P4; fixed-50%-cover projection P5. No real-site compliance or measured comfort result is claimed; method lead [4].
16
FIXED 50% PLAN COVER • SOLAR TIME 09:00 → 15:00
01
SEATING LOCATION
Use the occupied-hour footprint, not just the crown outline or shadow centroid.
02
SPACE FOR ACCESS & ROOTS
Allow for circulation, counterweight, root zone, irrigation and maintenance.
03
VALIDATE THE OUTCOME
Confirm site and planting; compare radiation, temperature, humidity and wind.
Notes: TAKEAWAY A practical layout must use the real occupied area, not only a reference square. SPOKEN SCRIPT The animation holds cover fixed while the sun moves. Seating should be checked during occupied hours, with room for circulation, the counterweight, roots and maintenance. The next verification step is a real-site assessment with simultaneous shaded and unshaded environmental observations. The current analysis does not establish net usable shaded floor area or a measured comfort improvement. TRANSITION The last design link is construction organisation. Q&A Are sensors a new project module here? No. This is the existing validation proposal, not a new monitoring-system design.

## Slide 17
GREEN BUILDING
MODULAR CONSTRUCTION
Coordinate prefabricated modules and site interfaces
Numbered components help assembly; long members, heavy base and grouted joints constrain it.
Project member/assembly and cost schedule (P3, P4). Proposed detail and labour quantities, not a tested construction programme.
17
MODULE | WHAT IS PREPARED
Crown | 47 formed/treatment-ready bamboo members
Supports | 12 proposed galvanised steel members
Connections | Head nodes, sleeves, clamps and base flange
Foundation | Precast counterweight with anchorage
Planting | 2 + 1 plants, substrate and drip provision
01
Prefab, treat & number
02
Lift base and set out
03
Support, align & assemble
04
Grout, cure & recheck
05
Plant, train & restore
14 person-days estimated ≠ 14 calendar days. The ≈9.07 t base controls lifting; grouted nodes limit lossless reversal.
Notes: TAKEAWAY The assembly work is more specific than a generic prefabrication claim. SPOKEN SCRIPT The proposal divides the system into crown members, supports, connections, base and planting. Numbering and preassembly help site organisation. However, the heavy counterweight governs lifting, and the sleeve-and-grout node requires curing and checks. The fourteen-person-day allowance is labour, not a calendar programme. A fully dry, losslessly reversible system should not be claimed. TRANSITION Finally, our delivered work and its next checks. Q&A Is the node a finished construction detail? No. Its geometry, stiffness, fabrication and quality controls need to be resolved together.

## Slide 18
GREEN BUILDING
WORK SUMMARY
Connect geometry, construction and useful shade
Three design workstreams now have traceable outputs.
Synthesis of project records P1–P5. Product, joint, site and growth-duration evidence are the next verification priorities.
18
GEOMETRY
Rhino/GH model and parameters
Final form, drawings and material take-off
MATERIALS & BUILD-UP
Screening, sections, budget and modules
Proposed interfaces and implementation constraints
PERFORMANCE
Time-dependent shade and sensitivity
Geometry, cover and spatial-distribution effects
7 PARAMETER MODELS
5 COVER STATES
1,750 TIME-STEP RESULTS
Next: confirm products and joints, calibrate plant establishment, and test the real site.
Notes: TAKEAWAY The contribution is a connected body of design work with a clear evidence boundary. SPOKEN SCRIPT The group delivers a parametric form and take-off, a proposed material and build-up strategy, and reproducible shade scenarios. The supplement adds seven parameter models, five cover states and seventeen hundred and fifty time-step results. These outputs make the design decisions traceable. Product data, joint behaviour, biological establishment and real-site performance are the next checks. Thank you. TRANSITION We welcome your questions. Q&A What can be stated most confidently? The defined project geometry and the calculated shade scenarios under their explicit assumptions.

## Slide 19
GREEN BUILDING
REFERENCES / Q&A
References and project evidence
Method sources and project inputs are separate; drawings, brief and schedules accompany the deck.
Literature entries were supplied with project records; original-source checks remain pending. Unverified factors are not presented as certified standards.
19
[1] OUTDOOR SHADE & COMFORT
Watanabe et al. (2014). Evaluation of outdoor thermal comfort in sunlight, building shade, and pergola shade during summer in a humid subtropical region. Building and Environment, 82, 556–565.
[2] GREENING MECHANISMS
Hoelscher et al. (2016). Quantifying cooling effects of facade greening: Shading, transpiration and insulation. Energy and Buildings, 114, 283–290.
[3] SOLAR GEOMETRY
NOAA Global Monitoring Division. General Solar Position Calculations.
gml.noaa.gov/grad/solcalc/solareqns.PDF
[4] COMFORT METHOD
UTCI Calculator / COST Action 730.
www.utci.org/utci_calc.php
Method lead only; no project UTCI result is reported.
PROJECT RECORDS
P1 Model & take-off • P2 Ideal shade analysis • P3 Cost-Analysis.xlsx
P4 Proposed design & build-up • P5 Parameter and spatial-cover simulation
The growth-time page deliberately has no month/year curve without species- and site-specific evidence.
Notes: TAKEAWAY Source labels let the audience distinguish literature, project calculations and proposals. SPOKEN SCRIPT This is a reference and question page, not part of the planned spoken sequence. It identifies the literature leads and project evidence. Specific product parameters and standards still require original-source checks. TRANSITION Return to the relevant result slide during questions. Q&A Why are some data preliminary? The supplied package contains assumptions and estimates that have not all been traced to product-specific or primary evidence.